ENGLISH : INSTRUCTIONS FOR USE

IMPORTANT: Single-use respirators against solid and liquid aerosols (e.g. oil-mists) are classified according to one of three categories- FFP1D, FFP2D and FFP3D. Before reading the following information, please check the category to which the respirators belongs-this is indicated on the packaging and on the respirator.

APPLICATIONS:

-FFP1D: protection against non-toxic solid and liquid aerosols (e.g. oil-mists) in concentrations up to 4.5 x MAC/OEL/TLV or 4 x APF.

-FFP2D: protection against non-toxic and low-to-average toxicity solid and liquid aerosols (e.g. oil-mists) in concentrations up to 12 x MAC/OEL/TLV or 10 x APF.

-FFP3D: protection against non-toxic, low-to-average toxicity and high toxicity solid and liquid aerosols (e.g. oil-mists) in concentrations up to 50x MAC/OEL/TLV or 20x APF.

PERFORMANCES: This single-use respirator meets the French requirements based on a loading test of 120mg and should not be used more than 8 hours time; however, it is established that the exact using length can not be exactly determined and depends on many factors: humidity rate, aerosol concentration rate, user’s breath and work difficulty carried out…Therefore, it is of user’s responsibility and none of the manufacturer’s to determine whether this product is suitable for the intended use.

FITTING INSTRUCTIONS:   Refer to the drawings matching the titles in this user instruction. 1. Hold the respirator in hand with the nosepiece at your fingertips. Allow headbands to hang freely below hand.  2. Cup the respirator firmly against your face with the nosepiece on the bridge of your nose. Stretch and pull the lower headband over the head and position below your ears. 3. Stretch and pull the top headband on the back of your head above your ears. Respirators with adjustable headbands only: while maintaining the position of the respirator, adjust tension by pulling tab of each headband. (Tension may be decreased by pushing out the back of the buckle).  4. Press soft nosepiece to conform snugly around the nose. CHECKING:  5. (a) To test fit for respirator without exhalation valve: Cup both hands over the respirator and exhale vigorously. 5. (b) To test fit for respirator with exhalation valve: Cup both hands over the respirator and inhale sharply. A negative pressure should be felt inside respirator. If air flows around your nose, tighten the nosepiece. If air leaks around the edges, reposition the headband for better fit.

LIMITATIONS: Change respirator immediately if breathing becomes difficult or respirator becomes damaged or distorted, or a proper face fit can not be maintained. Careful observance of these instructions is an important step in safe respirator use.

WARNING:  1. Failure to follow all instructions and limitations on the use of this product could reduce the effectiveness of respirator and result in sickness or death.

2. A properly selected respirator is essential to protect your health. Before using this respirator, consult an Industrial Hygienist or Occupational Safety Professional to determine the suitability for your intended use.

3. This product does not supply oxygen. Use only in adequately ventilated areas containing sufficient oxygen to support life. Do not use this respirator when oxygen concentration is less than 17%.

4. Do not use when concentrations of contaminants are immediately dangerous to health or life.

5. Do not use in explosive atmospheres.

6. Leave work area immediately and return to fresh air if (a) breathing becomes difficult, or (b) dizziness or other distress occurs.

7. Facial hairs or beards and certain facial characteristics may reduce the effectiveness of this respirator.

8. Never alter or modify this respirator in any way. There are no suitable spare parts.

ACCESSORIES: The effectiveness of this single-use respirator can not be hindered by other PPE (Personal Protective Equipment) use. The wearing of other PPE such as safety goggles, hooded coverall, ear muff protectors, helmets… is only possible when the effectiveness of the respirator is intact.

CLEANING, WASHING, MAINTENANCE AND DESINFECTION: Only for single use. No cleaning, no maintenance and no disinfection are necessary. Discard the used respirator after single use.

STORAGE AND TRANSPORT: Always store and transport respirators in the display box as delivered by the manufacturer; store the respirators away from direct sunlight until use.

VALIDITY DATE: Refer to the display box

If undone, join a copy of this sheet and transfer the validity date and lot number with each new smaller packing.

NOTE: MAC= Maximum Admissible Concentration       OEL= Occupational Exposure Limit

TLV= Threshold Limit Value                                APF= Assigned Protection Factor

D: the respirator pass the EN149:2001 optional dolomite (D) clogging test for more comfortable breathing.

MEANING OF PICTOGRAMS:

(1)	     (2)             (3)

(1)	See user information.

(2)	Recommended temperature condition of storage.

(3)	Recommended humidity condition of storage.

The CE marking has been shown to comply with the European PPE Directive 89/686/EEC.

Certified by British Standards Institution (BSI), Mayland Ave., Hemel Hempstead, Herts, HP2 4SQ, UK (Notified body No. 0086).

For more information, contact: EURO PROTECTION, 420 rue de la Dombes, 01700 Miribel, FRANCE